## Slide 1: Deep neural network for XPS data analysis
강원대학교 물리학과 박 형 선
Kangwon National University Department of Physics 양자시공간 연구실
제일원리 전자구조계산 연구실
박형선

## Slide 2
강원대학교 물리학과 박 형 선
Kangwon National University Department of Physics 양자시공간 연구실
1. Artificial Neural Network
Consist of Artificial neuron and edge
One artificial neuron is originated from single perceptron

## Slide 3
강원대학교 물리학과 박 형 선
Kangwon National University Department of Physics 양자시공간 연구실
2. Single Perceptron
Sing Perceptron architecture
Input data -> linear combination -> Activation function -> Output

## Slide 4
강원대학교 물리학과 박 형 선
Kangwon National University Department of Physics 양자시공간 연구실
3. Activation functions
Activation functions are, generally well tabulated
Sigmoid : classification
Tangent Hyperbolic : GAN
Relu – hidden layer

## Slide 5
강원대학교 물리학과 박 형 선
Kangwon National University Department of Physics 양자시공간 연구실
4. Backpropagation
Error = y_true – y_predict
Backpropagation to former layer

## Slide 6
강원대학교 물리학과 박 형 선
Kangwon National University Department of Physics 양자시공간 연구실
4. Backpropagation – Gradient Descent
Calculation of Gradient
Alpha : learning rate, hyper-parameter
MSE

## Slide 7
강원대학교 물리학과 박 형 선
Kangwon National University Department of Physics 양자시공간 연구실
5. MNIST
Classification example
Handwritten digit picture with labeling(One-hot vector)
Input : image, output : label

## Slide 8
강원대학교 물리학과 박 형 선
Kangwon National University Department of Physics 양자시공간 연구실
6. CNN(Convolutional Neural Network)
Weight update
SGD
Linear output
Activation function
Step1 : Feature extraction
Step2 : Neural network
Artificial Neural Network : Input layer + hidden layer + output layer
Direction : forward propagation, back propagation

## Slide 9
강원대학교 물리학과 박 형 선
Kangwon National University Department of Physics 양자시공간 연구실
General CNN architecture
General CNN architecture
Input[image] -> Conv2D -> Pooling -> Conv2D -> Pooling -> … -> FCL -> … -> output[label]

## Slide 10
강원대학교 물리학과 박 형 선
Kangwon National University Department of Physics 양자시공간 연구실
Convolution and Pooling
Convolution : Feature extraction using Kernel Matrix(filter)
(Max)Pooling : Sub-sampling, Feature compression

## Slide 11
강원대학교 물리학과 박 형 선
Kangwon National University Department of Physics 양자시공간 연구실
Convolution
Large value of convolution shows an existence of specific feature on the local area

## Slide 12
강원대학교 물리학과 박 형 선
Kangwon National University Department of Physics 양자시공간 연구실
7. XPS Data Analysis
DCNN to detect and quantify chemical elements in experimental XPS data
XPS : Surface sensitive technique providing element analysis of topmost 10nm layer

## Slide 13
강원대학교 물리학과 박 형 선
Kangwon National University Department of Physics 양자시공간 연구실
Basic Principle

## Slide 14
강원대학교 물리학과 박 형 선
Kangwon National University Department of Physics 양자시공간 연구실
XPS Data
Experimental device using Photoelectric effect to get B.E. of electrons

## Slide 15
강원대학교 물리학과 박 형 선
Kangwon National University Department of Physics 양자시공간 연구실
Figure 2. Synthetic Spectra data
(a) : An excerpt of two simulated survey training spectra
(b) : Maximum XPS intensity of simulated spectra for each pure element,
calculated for a fixed photon fulx,
photon energy = 1486.6eV, K.E. spectra range = 400 ~ 1486eV

## Slide 16
강원대학교 물리학과 박 형 선
Kangwon National University Department of Physics 양자시공간 연구실
Figure 3. Deep neural network layout
Inception module version 4
f : the filter number, k : convolution kernel size, s : stride length
Total trainable parameters : 4366410

## Slide 17
강원대학교 물리학과 박 형 선
Kangwon National University Department of Physics 양자시공간 연구실
Inception Module
Inception module (in GoogLeNet) at ILSVRC 14
Parallel operation of convolution filter
Sparse Connectivity architecture <-> CNN FCL(dense layer)

## Slide 18
강원대학교 물리학과 박 형 선
Kangwon National University Department of Physics 양자시공간 연구실
Figure 4. Loss function convergence in training
Case with “No dropout, and standard L2(Ridge) norm (over-fitting)
Case with a 15% dropout before classification layer, and high-pass norm optimizal p range = 0.1 ~ 0.2

## Slide 19
강원대학교 물리학과 박 형 선
Kangwon National University Department of Physics 양자시공간 연구실
Result.
Application examples on two experimental sets; spectra(a) and quantification(b)
for carbon nanotubes on SI; spectra(c) and
quantification (d) for indium-tin oxide(ITO) deposited on Si.
For ITO case, the adventitious carbon contamination was factored out from the experimental quantification

## Slide 20
강원대학교 물리학과 박 형 선
Kangwon National University Department of Physics 양자시공간 연구실
Result. Positive identification ratio
Positive identification ratio of DNN versus the quantification output :
calculated for the experimental data(red) and a synthetic training set(black)

## Slide 21
강원대학교 물리학과 박 형 선
Kangwon National University Department of Physics 양자시공간 연구실
Result. Carbon quantization
  Full carbon experimental quantification(red) and corresponding results for the DNN(black)
  It has been trained to ignore carbon from adventitious contamination

## Slide 22
강원대학교 물리학과 박 형 선
Kangwon National University Department of Physics 양자시공간 연구실
Peak Detection and Fitting
Objective : Automation of Peak fitting using machine learning
Useful features : number of peak, mean position, FWHM, intensity, area etc

## Slide 23
강원대학교 물리학과 박 형 선
Kangwon National University Department of Physics 양자시공간 연구실
Filter visualization and convolution result

## Slide 24
강원대학교 물리학과 박 형 선
Kangwon National University Department of Physics 양자시공간 연구실
Filter visualization and convolution result

## Slide 25
강원대학교 물리학과 박 형 선
Kangwon National University Department of Physics 양자시공간 연구실
Peak Detection and Fitting
One input, two ouput

## Slide 26: 감사합니다
강원대학교 물리학과 박 형 선
Kangwon National University Department of Physics 양자시공간 연구실
Reference : Deep nerual network for x-ray photoelectron spectroscopy data analysis